## Slide 1: SimPowerSystems Hands-on Workshop: Modeling and Simulation of Electrical Power Systems with SimPowerSystemsTM
Carlos Osorio
Principal Application Engineer
MathWorks – Natick, MA
5. Control of Electrical Machines

## Slide 2: Outline
Electrical disturbances
  Emergency generator example
Control of synchronous generators
  Generator droop control example
  Load sharing example
  Breaker synchronization example
Electric motor drives

## Slide 3: Electrical disturbances Emergency generator example
>> emergency_generator

## Slide 4: Electrical disturbances Emergency generator example
Switch the simulation to phasor mode to speed up any additional testing of the system
>> emergency_generator
1
2
4
Examine the components in the generator control subsystem and identify the library that contains additional exciter models
Run a Load Flow initialization to start the simulation of the system from steady-state
3
Verify the performance of the generator after the fault occurs at 0.1 seconds and identify how long it takes for the motor to fully recover

## Slide 5: Synchronous generator control Generator droop control example
>> single_generator_droop

## Slide 6: Synchronous generator control Generator droop control example
>> single_generator_droop
2.5% droop
@ 100% load
1
2
1
2

## Slide 7: Synchronous generator control Load sharing example
>> two_generator_droop
The increase in load will be shared by the two generators based on their power ratings and their droop settings

## Slide 8: Synchronous generator control Load sharing example
>> two_generator_droop
1
2
2
2
1
1% droop
20%
25%

## Slide 9: Synchronous generator control Breaker synchronization example
>> synchronizing_breaker

## Slide 10: Synchronous generator control Breaker synchronization example
>> synchronizing_breaker
For numerical stability, always approximate a no-load condition by attaching a small shunt – between 1% and 5% of nominal –
at the output of the generator
When using Discrete simulation mode, you can choose the Trapezoidal Iterative algorithm to maintain solver stability with smaller shunts

## Slide 11: Synchronous generator control Breaker synchronization example
>> synchronizing_breaker
There are two stages for synchronizing an incoming generator:
Establish the frequency of the incoming generator slightly above the bus frequency – within some tolerance
Connect when the voltage of the incoming generator is in-phase and equal in magnitude to the bus voltage – within some tolerance
1
2
frequency
synch
phase
synch
1
2
synchronization
enabled
connection
made
generator
goes off-line

## Slide 12: Synchronous generator control Breaker synchronization example
>> synchronizing_breaker
3
Examine the controller for an example of how management strategies for multiple circuit breakers can be easily implemented using state machine logic

## Slide 13: Synchronous generator control Breaker synchronization example
>> synchronizing_breaker_mref
Place the controller in a separate model by converting the subsystem to a Model Reference
Subsystem & Model Reference  Convert Subsystem to  Referenced Model
4
5
Switch the simulation mode for the controller to Accelerator
Block Parameters (Model Reference)  Simulation mode

## Slide 14: Synchronous generator control Breaker synchronization example
>> synchronizing_breaker_mref
Force an unsynchronized connection at 1.5 seconds by using the override signal
6
5
5

## Slide 15: Synchronous generator control Generator no-load test – Simscape Components
>> generator_noload_ssc
The synchronous machine blocks in the Simscape Components library allow testing of no-load conditions without requiring a generator shunt

## Slide 16: Electric motor drives Application libraries
Contain a variety of prebuilt AC and DC motor drive models that can be used directly or as starting templates

## Slide 17: Electric motor drives Variable frequency drive
>> pmsm_drive_st

## Slide 18: Electric motor drives Variable frequency drive – Simscape Components
>> pmsm_drive_ssc
Transistors can be quickly replaced with detailed nonlinear models from the SimElectronics library