## Slide 1
Steve Miller
Technical Marketing, Physical Modeling
MathWorks
http://www.mathworks.com/physical-modeling/
GEN
AC1
AC2
AC3
TRU
DC1
DC2
DC3
Batt
AC Bus
DC Bus
Aircraft Power Network Development with Model-Based Design
DETAILED
Electrical
DESIGN
SYSTEM LEVEL MODEL
Control
Mechanical
Electrical
ϕ
REQUIREMENTS

## Slide 2: Key Points
Configure your model to balance model fidelity and simulation speed
Accelerate your simulations using optimization algorithms and parallel computing
Accelerate your development by automating simulation and analysis tasks using MATLAB®
Computational
Time
Detail
Computational Time vs. Model Complexity
Network Model
Multi
Core

## Slide 3: Agenda
Overview: Aircraft Power Network Model
  Simulation goals
  Development process
Initial Design
  Linking to requirements
  Refining requirements
Detailed Design
  Generators, loads
  Harmonic analysis
  Integrating other domains
Tuning Abstract Model
Documenting Results

## Slide 4: Aircraft Power Network System for Analysis
Half-aircraft model
  One generator
  AC bus with loads
  TRU (Transformer- Rectifier Unit)
  DC bus with loads and battery
Breakers open and close during flight cycle
Breaker
GEN
APU
External Power
Not modeled
AC3
AC2
AC1
DC3
DC2
DC1
Batt
AC Bus
DC Bus
GEN
TRU

## Slide 5: Aircraft Power Network Simulation Goals
Determine power requirements
  Generator, loads, battery
  Power lines
Analyze system interactions
  Electrical, mechanical, hydraulic, thermal, etc.
Perform harmonic analysis
  Varying conditions
  Voltage and current at different nodes in network
Breaker
GEN
APU
External Power
Not modeled
AC3
AC2
AC1
DC3
DC2
DC1
Batt
AC Bus
DC Bus
GEN
TRU

## Slide 6: Aircraft Power Network Simulation Results
Results from system-level and detailed models match
Enables rapid iteration at system level and detailed analysis of electrical system

## Slide 7: Aircraft Power Network Simulation Model
Generator
  Integrated Drive
  VSCF Cycloconverter
  VSCF DC Link
AC Loads
  Detailed
  Abstract
DC Loads
  Detailed
  Abstract
  Multidomain

## Slide 8: Balancing Fidelity and Simulation Speed
Key to effective use of simulation
  Capture only the effects you need
  Configure the model for your task
MathWorks products enable you to select the right level of detail for your task
Computational Time
Model Complexity & Detail
Computational Time vs. Model Complexity
Configure your model to balance simulation speed and model fidelity.
Abstract Loads
Phasor Simulation
Averaged Voltage
Realistic Loads
PWM Control
Power
Electronics

## Slide 9: Balancing Fidelity and Simulation Speed System and Component Level Design
Design process requires abstract and detailed models
  Refine requirements (system level)
  Design component
  Combine as necessary
  Tune abstract model for rapid simulation
System and detailed models are complementary
  Match level of detail to simulation task
DETAILED
Electrical
SYSTEM LEVEL MODEL
Control
Mechanical
Electrical
ϕ
2
3
1
REQUIREMENTS
4

## Slide 10: Airbus Develops A380 Fuel Management System Using Model-Based Design
Challenge
Develop a controller for the Airbus A380 fuel management system.
Solution
Use MATLAB and Simulink to model and simulate the control logic, communicate the functional specification, and accelerate the development of simulators.
Results
100,000 tests run in parallel each weekend
Months of development time eliminated
Models reused throughout development
Additional complexity handled without staff increases
“Model-Based Design gave us advanced visibility into the functional design of the system. We also completed requirements validation earlier than was previously possible and simulated multiple simultaneous component failures, so we know what will happen and have confidence that the control logic will manage it.”
Christopher Slack Airbus
Link to user story
Notes: Primary Industry: Aerospace and Defense
Secondary Industries: N/A
Product Capabilities: Mathematical modeling, Algorithm development, Parallel computing, System design and simulation, Physical modeling, Verification, validation, and test
Applications: Embedded systems, Control systems, Digital signal processing
Products Used: MATLAB, Simulink, Curve Fitting Toolbox, MATLAB Distributed Computing Server, Parallel Computing Toolbox, Signal Processing Toolbox, SimPowerSystems, Simulink Coder, Stateflow, System Identification Toolbox
Country: United Kingdom
Airbus Develops Fuel Management System for the A380 Using Model-Based Design
The Airbus A380, the largest commercial aircraft currently in operation, has a range of more than 8,000 miles. To enable such long non-stop flights, the A380’s 11 fuel tanks have a capacity of 250 metric tons (320,000 liters).
The A380’s sophisticated fuel management system handles fueling and defueling operations on the ground, as well as fuel flow to engines and between tanks while airborne. The system can move fuel between tanks to optimize the aircraft’s center of gravity, reduce wing bending, and keep fuel within the acceptable temperature range.
Airbus engineers used Simulink® and Stateflow® to develop a model of the fuel management system that was reused throughout the project. “With Model-Based Design, the model we used to represent the functional specification enabled us to validate requirements months earlier than was previously possible,” says Christopher Slack, computational analysis expert in fuel systems at Airbus.
The Challenge
The A380’s fuel management system must be able to safely handle any failure in the system’s 21 pumps, 43 valves, and other mechanical components. In a complex system, it’s challenging for engineers at the requirements stage to predict any problem that can result from combinations of relatively minor failures.
The fuel system specification document for the A380’s predecessor, the A340, had over a thousand written requirements. “Text requirements can leave room for ambiguity and misinterpretation. When you have that many requirements, it’s difficult for anyone to understand all the possible interactions between them and identify, for example, that a requirement on page 20 conflicts with one on page 340,” says Slack.
    “Model-Based Design gave us advanced visibility into the functional design of the system. We also completed requirements validation earlier than was previously possible and simulated multiple simultaneous component failures, so we know what will happen and have confidence that the control logic will manage it.”
    - Christopher Slack, Airbus
The Solution
Airbus used Model-Based Design to model the A380’s fuel management system, validate requirements through simulation, and clearly communicate the functional specification.
Airbus engineers used Simulink and Stateflow to model the system’s control logic, which comprises 45 top-level charts, almost 6000 states, and more than 8700 transitions. This model defines modes of operation on the ground (including refuel, defuel, and ground transfer) and in flight (including normal engine feed, center of gravity control, load alleviation, and fuel jettison).
The functionality within each top-level mode is grouped into subcharts, enabling engineers to work independently on individual components in the hierarchy.
The team developed a parameterized plant model of the tanks, pumps, valves, and electrical components using Simulink. Engineers can set parameter values to configure this model to represent fuel systems for any Airbus aircraft.
After running closed-loop simulations of individual operational components in Simulink, the team integrated them into a complete model for system-level simulations.
Using Parallel Computing Toolbox™ and MATLAB Distributed Computing Server™, the team performed Monte Carlo simulations on a 50-worker computing cluster. Over a weekend, they can run 100,000 simulated flights under varied environmental conditions and aircraft operational scenarios.
The team created a desktop simulator by generating code from the plant and control logic models with Simulink Coder™. A MATLAB® based user interface enables suppliers, airline customers, maintenance engineers, and other Airbus teams to visualize how the fuel management system works and interacts with other aircraft systems.
The team also used the Simulink models to develop hardware-in-the-loop (HIL) tests and commission their HIL testing rig well before the real hardware was available.
After successful flight tests of the A380, the team used System Identification Toolbox™ to tune their plant model using measured flight test data. They used Signal Processing Toolbox™ to remove noise from the test data, and Curve Fitting Toolbox™ to evaluate differences between the measured data and predicted results and to predict system performance beyond the usual flight envelopes. While refining the plant model, they used SimPowerSystems™ to incorporate relays and other elements of the electrical power system.
Based on the success of implementing Model-Based Design for the A380, Airbus engineers are now using this approach to develop the Airbus A350XWB’s fuel management system, reducing development time of this aircraft by one year.
The Results
■ Months of development time eliminated. “On earlier projects, it took up to nine months to integrate our fuel system design with the simulated cockpit, or iron bird. Using Model-Based Design on the A380, it took less than a month,” says Slack. “Similarly, by reusing the model to commission the HIL rig, we saved three months of development and shortened the time from initial concept to first flight.”
Models reused throughout development. “The Simulink and Stateflow models enabled us to validate requirements early and communicate the functional specification to our suppliers, complementing the written requirements in conformance with ARP 4754,” says Slack. “These models were reused to create desktop simulators, commission our HIL test rig, run on our virtual integration bench, and demonstrate system functionality to customers.”
Additional complexity handled without staff increases. “The fuel system of the A380 is three to four times more complex than that of the A340,” notes Slack. “Model-Based Design enabled us to handle a substantially more complex project with the same size engineering team.”
Learn more about Airbus: www.airbus.com

## Slide 11: Agenda
Overview: Aircraft Power Network Model
  Simulation goals
  Development process
Initial Design
  Linking to Requirements
  Refining Requirements
Detailed Design
  Generators, Loads
  Harmonic analysis
  Integrating other domains
Tuning Abstract Model
Documenting Results
SYSTEM LEVEL MODEL
Control
Mechanical
Electrical
ϕ
DETAILED
Electrical
2
REQUIREMENTS
1

## Slide 12: Linking Specification and Design
Problem: Difficult to compare design and specification.
Solution: Use Simulink
Verification and Validation to link the design and specification.
Situation:
Part Numbers
Power Network Req.
1. Network Schematic
Notes: http://inside.mathworks.com/gallery/v/creativeservices/IndustriesAndApplications/AeroDef/Aircraft/jet_silo.jpg.html mw copyright own

## Slide 13: Refining Requirements for Power Network
Operating, peak, and design loads for generators and lines
  Wide range of network conditions
  Neglect power electronic switching
Use abstract models and simulation methods
AC3
AC2
AC1
DC3
DC2
DC1
Batt
AC Bus
DC Bus
GEN
TRU
Flight Cycle 1
Flight Cycle 2
…
Loads On/Off
…
Hours
Computational Time
Model Complexity & Detail
Abstract Loads
Phasor Simulation
Averaged Voltage
Realistic Loads
PWM Control
Power
Electronics

## Slide 14: Simulation Modes
Continuous: variable-step size
  Accurate: step size shrinks to capture events
  Speed depends on # of continuous states and dynamics
Discrete: fixed-step size
  Fewer computations per step
  Very scalable, good for large systems
Phasor: simplified set of equations
  Uses algebraic equations to represent voltage and current as phasor
  Very fast, but solution only at a specific frequency
Continuous
Discrete
Phasor

## Slide 15: Selecting Simulation Mode
Problem: Analyze transient effects and magnitudes of circuit voltages
Solution: Select the SimPowerSystems™ simulation mode that is appropriate for the analysis
Situation:

## Slide 16: Generic Abstract Model AC Loads, Sources
Dynamic Load provides generic abstract model
  Specify active and reactive powers by signal or voltage sequence
  Use to define source or load
  Define initial abstract model based on requirements
Ideal source enables calculation of generator requirements

## Slide 17: Refining Power Requirements for Generator, Lines
Problem: Refine initial requirements by testing a wide range of conditions
Solution: Use abstract loads, sources, and phasor simulation to refine power requirements
Situation:
1
2
3
4
5
6
1
2
3
4
5
6
Cycle 1
Cycle 2
…
Loads On/Off
…
Hours

## Slide 18: Agenda
Overview: Aircraft Power Network Model
  Simulation goals
  Development process
Initial Design
  Linking to Requirements
  Refining Requirements
Detailed Design
  Generators, Loads
  Harmonic analysis
  Integrating other domains
Tuning Abstract Model
Documenting Results
DETAILED
Electrical
2
SYSTEM LEVEL MODEL
Control
Mechanical
Electrical
ϕ
REQUIREMENTS
1
3

## Slide 19: Aircraft Power Generation Options
Several options currently in use (commercial, military)
Common components:
  Generator
  Power electronics to convert power
Integrated Drive Generator
VSCF1 Gen., Cycloconverter
VSCF Gen., DC Link
1Variable Speed Constant Frequency
400 Hz
AC
Constant
Speed Drive
400 Hz
AC
Cyclo- conv.
400 Hz
AC
DC
Variable Frequency Generator
400 - 800 Hz
AC

## Slide 20: Power Generation Machines Library
Many types provided
  Synchronous, Asynch., PMSM…
  Excitation models (AC1A, etc.)
Many parameterization options
  Types, phases, inputs …
  Preset models
  Enable/Disable effects

## Slide 21: Power Electronics
Many devices provided
  Diode, thyristor, IGBT, MOSFET
  PWM and signal generators
Configurable bridges
  Select device type
  Switching function and Average-model options for increased speed
  Log internal measurements

## Slide 22: Modeling Power Generation
Problem: Evaluate options for generating AC power for network
Solution: Use SimPowerSystems to model, simulate, and evaluate options
Situation:
400 Hz
AC
Cyclo- conv.
400 Hz
AC
DC
Turbine (variable speed)

## Slide 23: AC Loads
Options for AC loads include:
  RLC loads and branches
  Transformers
  Machines
  Drives (machine + converter + control)
Many configuration options
  Configurations and fidelity

## Slide 24: Analyzing Power Quality Total Harmonic Distortion (THD)
Loading can cause distortion of supply voltage waveform
Effects of poor power quality
  Heating in generator
  High neutral currents
  Unnecessary switching in power electronics
THD provides a measure of AC power quality
  Important to measure under varying network conditions
  Easy to calculate with MathWorks products

## Slide 25: Analyzing Power Quality
Problem: Evaluate power quality within network under various conditions
Solution: Use SimPowerSystems and MATLAB to automate calculation of total harmonic distortion (THD)
Situation:
GEN
AC1
AC2
AC3
TRU
DC1
DC2
DC3
Batt
AC Bus
DC Bus
1
2
Loads On/Off
…
Hours
Voltage

## Slide 26: DC Loads
Pure electrical and multidomain options
Multidomain
Electrical + Thermal
Electrical + Mechanical + Hydraulic

## Slide 27: Modeling Physical Systems
Foundation library of physical elements
  Mechanical, hydraulic, electrical…
Create custom components using Simscape™ Language
Simscape
Mechanical
Hydraulic
Electrical
Thermal
Custom Domains via Simscape Language
Pneumatic
Magnetic
N
S
P
T
A
B

## Slide 28: Simscape Add-on Libraries
Multidomain
physical systems
SimMechanics
SimDriveline
SimHydraulics
SimElectronics
SimPowerSystems
Simscape
MATLAB, Simulink
Simscape
Mechanical
Hydraulic
Electrical
Thermal
Custom Domains via Simscape Language
Pneumatic
Magnetic
N
S
SimDriveline™
  Gears, leadscrew, clutches, tires, engines
SimElectronics®
  Actuators, sensors, and semiconductors
SimHydraulics ®
  Pumps, actuators, pipelines, valves, tanks
SimMechanics™
  Multibody systems: joints, bodies, frames
SimPowerSystems™
  Three-phase electrical networks

## Slide 29: Agenda
Overview: Aircraft Power Network Model
  Simulation goals
  Development process
Initial Design
  Linking to Requirements
  Refining Requirements
Detailed Design
  Generators, Loads
  Harmonic analysis
  Integrating other domains
Tuning Abstract Model
Documenting Results
SYSTEM LEVEL MODEL
Control
Mechanical
Electrical
ϕ
4
DETAILED
Electrical
2
REQUIREMENTS
3
1

## Slide 30: AC Loads Tune Abstract Model
Need to refine initial abstract model to match detailed simulation results
  Specify active and reactive powers using input signal
  Tune to match behavior of detailed design
Initial Abstract Model
Tuned Abstract Model

## Slide 31: Tuning Abstract Models to Match Detailed Results
Problem: Result from abstract model do not match detailed simulation results
Solution: Use Simulink Design Optimization to automatically tune model parameters
Situation:
DETAILED
ABSTRACT
ϕ
Control Signal
Active Power
Reactive Power
Active Power
Reactive Power
slope | step_down | q_scaling
792 | 250 | 0.72
slope | step_down | q_scaling
2432 | 452.3 | 0.2713

## Slide 32: Tuning Abstract Models to Match Detailed Results
Steps to Estimate Parameters
  Import measurement data and select estimation data
  Identify parameters and their ranges
  Perform parameter estimation
  Validate estimation
slope | step_down | q_scaling
792 | 250 | 0.72

## Slide 33: Tuning Abstract Model
Video of Parameter Tuning

## Slide 34: Distributing Simulations with Parallel Computing
Simulating in parallel
  Distribute simulations to multiple cores/processors
  Dramatic speedup for sets of simulations (parameter sweeps, flight cycles optimizations, and more)
…
Computer Cluster
Workers
…
…
Running simulations in parallel speeds up your testing process.
Desktop System
Workers
…
…
Simulation 1
Simulation 2
for parfor
Network Model

## Slide 35: Accelerate Flight Cycle Tests Using Parallel Computing
Problem: Test system performance under a range of conditions (flight cycles, faults, weather, etc. )
Solution: Use Parallel Computing Toolbox™ to speed up the set of tests
Model:
Parameter Set 1
Parameter Set 2
Parameter Set N
…
GEN
AC1
AC2
AC3
TRU
DC1
DC2
DC3
Batt
AC Bus
DC Bus
Flight Cycles
Faults
Equipment
Weather
…
Multi
Core

## Slide 36: Accelerate Flight Cycle Tests Using Parallel Computing
Steps to compare simulation methods
1. Open pool of MATLAB sessions
2. Generate parameter sets
3. Run simulations serially
4. Run simulations in parallel
Parameter Set 1
Parameter Set 2
Parameter Set N
…
>> matlabpool
Flight_Cycle_array = [1:8];
Generate_Sim_Settings
for i = 1:numSims
out{i} = sim(mdl, SimSettings{i});
end
parfor i = 1:numSims
out{i} = sim(mdl, SimSettings{i});
end
Multi
Core

## Slide 37: Agenda
Overview: Aircraft Power Network Model
  Simulation goals
  Development process
Initial Design
  Linking to Requirements
  Refining Requirements
Detailed Design
  Generators, Loads
  Harmonic analysis
  Integrating other domains
Tuning Abstract Model
Documenting Results
SYSTEM LEVEL MODEL
Control
Mechanical
Electrical
ϕ
4
DETAILED
Electrical
2
REQUIREMENTS
3
1

## Slide 38: Automatically Run Tests And Document Results
Problem: Evaluate test results quickly to make design changes and document the results
Solution: Use Simulink Report Generator to automatically document tests and results
Situation:
Design Change
Test
Evaluate Results
Document
Simulation 1
Simulation 2
…
Report
 Fail
Pass
Screenshots
C and MATLAB
Code
Plots and Results
Network Model

## Slide 39: Key Points
Configure your model to balance model fidelity and simulation speed
Accelerate your simulations using optimization algorithms and parallel computing
Accelerate your development by automating simulation and analysis tasks using MATLAB
Computational
Time
Detail
Computational Time vs. Model Complexity
Network Model
Multi
Core

## Slide 41: Refine Requirements Example Generator and Line Sizing
Refine operating, peak, and design load requirements
1
2
3
4
5
6
1
2
3
4
5
6

## Slide 42: Simulation Mode Example AC Circuit, Single Phase
Continuous, discrete, phasor
Compare results, speed

## Slide 43: Synchronous Machine Example
Mechanical power as input
Constant power AC load
Use Load Flow to set initial conditions

## Slide 44: Power Electronics Example AC-AC Conversion
VSCF Gen. with Cycloconverter
  2 Universal Bridges per phase
  AC-AC conversion
x3

## Slide 45: Power Electronics Example AC-DC-AC PWM
VSCF Generator with DC Link
Rectifier, inverter with PWM
Diode measurements

## Slide 46: Agenda
Overview: Aircraft Power Network Model
  Simulation goals
  Development process
Modeling
  Power generation and distribution
  Loads (AC, DC) and Battery Modeling
  Tuning abstract models
Simulation
  Modes (phasor/discrete, parallel simulations)
  Harmonic analysis
  Report generation

## Slide 47: Analyzing Power Quality Example Calculating THD
Tools for calculating THD
  Interactive GUI
  Scripting function
  During simulation

## Slide 48: Modeling the Mechanical System
Problem: Model the mechanical system within Simulink
Solution: Use SimMechanics to model the aileron
Model:
θ
Aileron

## Slide 49: DC System Battery
Challenge | Capability or Strategy
1. Hard to model exact electrochemical behavior | Approximate behavior with simplified equations or equivalent circuits
2. Multidomain, nonlinear effects are challenging to model | Use physical modeling tools to define equations and components
3. Model must simulate quickly to enable extensive testing (drive cycles, temperatures, etc.) | Include/neglect effects as needed to balance tradeoff of model fidelity and simulation speed
4. Model must provide results that compare well to test data | Use optimization algorithms to automatically tune parameter values until simulation results match test data
Challenge | Capability or Strategy
1. Hard to model exact electrochemical behavior | Approximate behavior with simplified equations or equivalent circuits
2. Multidomain, nonlinear effects are challenging to model | Use physical modeling tools to define equations and components
3. Model must simulate quickly to enable extensive testing (drive cycles, temperatures, etc.) | Include/neglect effects as needed to balance tradeoff of model fidelity and simulation speed
4. Model must provide results that compare well to test data | Use optimization algorithms to automatically tune parameter values until simulation results match test data
Tuning Capabilities
Modeling Methods
Battery
DC3
DC2
DC1
DC Bus

## Slide 50: Battery Models: Generic, Pre-Defined
Generic
  Charge dependent voltage source
  Parameters found on data sheets
Pre-Defined
  Several pre-defined models
  Full parameterization
  Documentation provides extensive detail

## Slide 51: Battery Models: Custom Cell
Use supplied components or build new components via Simscape language
Battery cell equivalent discharge circuit
Resistors, capacitor, and voltage source are dependent upon SOC, DOC, and temperature

## Slide 52: Simscape Language For Modeling Custom Components
MATLAB-based language, for text-based authoring of physical modeling domains, components, and libraries
  Leverages MATLAB
  Object-oriented for model reuse
  Generate Simulink blocks
  Save as binary to protect IP

## Slide 53: Estimating Parameters Using Measured Data
Problem: Simulation data does not match measured data because the parameters are incorrect
Solution: Use Simulink Design Optimization to automatically tune model parameters
Model:
A22 | Ao | Emo | Qe_init
-4 | -1 | 2 | 1.0e4
A22 = Constant
Ao = Constant
Emo = Open Cir. Voltage
Qe_init = Initial Extr. Chg.
A22 | Ao | Emo | Qe_init
-9.99 | 0.402 | 2.20 | 3.84e4
Battery Cell
Discharge Cycle
Voltage
Ambient Temperature

## Slide 54: Estimating Parameters Using Measured Data
Steps to Estimate Parameters
  Import measurement data and select estimation data
  Identify parameters and their ranges
  Perform parameter estimation
  Validate estimation
A22 | Ao | Emo | Qe_init
-4 | -1 | 2 | 1.0e4

## Slide 55: Tuning Models Additional Strategies and Capabilities
Tune parameters in stages
  Narrowing range for values
  Tune sets of parameters
  Tune with different data sets
Use scripting to automate tuning process
Accelerate parameter tuning by using parallel computing
Multi
Core