## Slide 1: SimPowerSystems Hands-on Workshop: Modeling and Simulation of Electrical Power Systems with SimPowerSystemsTM
Carlos Osorio
Principal Application Engineer
MathWorks – Natick, MA
4. Simulation Performance

## Slide 2: Outline
Model fidelity vs. simulation speed
SimPowerSystems simulation modes
  Inter-machine oscillation example
  Matrix converter example
  Power inverter example

## Slide 3: Model fidelity vs. simulation speed
Configure your model to balance the trade-off between simulation speed and model fidelity based on the goals of your simulation
Computation Time
Model Complexity & Detail
Averaged Voltage
High Frequency Switching
Computation Time vs. Model Complexity
Abstract Loads
Phasor Simulation
Realistic Loads
Nonlinear
Power
Electronics

## Slide 4: SimPowerSystems simulation modes
>> edit test_simulation_modes

## Slide 5: SimPowerSystems simulation modes Inter-machine oscillation example
>> inter_machine_oscillation

## Slide 6: SimPowerSystems simulation modes Inter-machine oscillation example
When there is no active control, the frequency will drop when the load R2 is connected
This will result in the phasor model results becoming increasingly inaccurate the further the frequency moves away from nominal
If active control* is in place, then the phasor simulation method is very effective for fast, credible results (*Note: in this example voltage regulators were excluded for clarity)

## Slide 7: SimPowerSystems simulation modes Inter-machine oscillation example
Simulation Mode | Normalized Time
Continuous | 0.788
Discrete Ts = 1e-04 | 1
Phasor | 0.034
>> edit bench_inter_machine_oscillation

## Slide 8: SimPowerSystems simulation modes Matrix converter example
Note: Phasor mode is not supported for systems with power electronic devices
>> threephase_matrix_converter

## Slide 9: SimPowerSystems simulation modes Matrix converter example
Simulation Mode | Normalized Time (Normal Mode) | Normalized Time (Accelerator Mode)
Continuous | 1 | 0.220
Discrete Ts = 2.5e-06 | 0.128 | 0.024
>> edit bench_threephase_matrix_converter

## Slide 10: SimPowerSystems simulation modes Discrete mode - Selecting the integration step size
circuit dynamics
switching frequency (fpwm)
duty cycle resolution (fs)
x 10…20
x 100…500
Tpwm
Tpwm
Ts
………..
?

## Slide 11: SimPowerSystems simulation modes Power inverter example
>> threephase_power_inverter

## Slide 12: SimPowerSystems simulation modes Power inverter example
>> edit bench_threephase_power_inverter
Simulation Mode | Normalized Time
Continuous | 1
Continuous Ideal Switches | 0.279
Discrete Ts = 1e-06, Normal Mode | 0.285
Discrete Ts = 1e-06, Accelerator Mode | 0.071