## Slide 1: SimPowerSystems Hands-on Workshop: Modeling and Simulation of Electrical Power Systems with SimPowerSystemsTM
Carlos Osorio
Principal Application Engineer
MathWorks – Natick, MA
6. Custom Electrical Components

## Slide 2: Outline
Simulink-based electrical components
Modifying Specialized Technology library components
Simscape Language and Simscape Components library
Simscape and SimPowerSystems interfaces
Model sharing and IP protection

## Slide 3: Simulink-based electrical components Controlled voltage and current sources
The voltage across the source terminals equals the input Simulink signal, regardless of the current requirement
The current through the source terminals equals the input Simulink signal, regardless of the voltage requirement
>> controlled_voltage_source
>> controlled_current_source

## Slide 4: Simulink-based electrical components Photovoltaic solar cell example
Where:
Iph Solar induced current (proportional to irradiance)
Is Diode saturation current (exponential behavior)
N Diode quality factor (emission coefficient)
Vt Thermal voltage kT/q (k: Boltzmann constant, T: device temperature)
Rp Shunt resistance (models leakage currents, primarily due to defects)
Rs Series resistance (models bulk and contact resistances)
exponential diode

## Slide 5: Simulink-based electrical components Photovoltaic solar cell example
>> sps_solarcell
SPS diode is modeled as a piecewise linear switch

## Slide 6: Simulink-based electrical components Photovoltaic solar cell example
Always need to properly break the algebraic loop
>> sl_solarcell

## Slide 7: Modifying Specialized Technology library components Custom synchronous machine example
Original machines library
powerlib/Machines
Break the link and save the original block to a user defined library
i.e. mySMBlocks_userDefinedLib
1

## Slide 8: Modifying Specialized Technology library components Custom synchronous machine example
Copy the underlying machine model library to a new user defined library
i.e. spsSynchronousMachineModel  mySMModels_userDefinedLib
2

## Slide 9: Modifying Specialized Technology library components Custom synchronous machine example
3
Modify any of the blocks in this new library and update the configurable subsystem template blocks
i.e. mySMModels_userDefinedLib
Replace the configurable subsystem templates under the mask of the original block with your modified templates
i.e. mySMBlock
4

## Slide 10: Simscape Language and Simscape Components library Three-phase electrical domain
>> simscape_custom_generator
Leverage the Simscape Language and the three-phase electrical domain to create custom components

## Slide 11: Simscape and SimPowerSystems interfaces Interfacing electrical domains
>> sps2se_pvinverter_avg
>> sps2se_pvinverter_det

## Slide 12: Simscape and SimPowerSystems interfaces Interfacing electrical domains
>> sps2se_pvinverter_avg
>> sps2se_pvinverter_det
Use the appropriate filter in the interface block to break the algebraic loop
Use the Simscape local solver to simulate slower dynamics
1
2

## Slide 13: Model sharing and IP protection Simscape Editing Mode
Function | Full Mode | Restricted Mode
Add or delete regular Simulink blocks | Yes | Yes
Change Simulink solver, simulate | Yes | Yes
Change numerical parameters | Yes | Yes
Access PowerGUI functions, settings | Yes | Yes
Generate code | Yes | Yes
Add/delete blocks from SimPowerSystems | Yes | No
Make or break physical connections | Yes | No
Change block parameterization options | Yes | No
Model Developer
Simscape license
SimPowerSystems license
Model Users
Simscape license
SimPowerSystems installed, but no license required
Model using Simscape and SimPowerSystems
Share SimPowerSystems models with other Simscape users
Simulate, analyze and generate code without requiring an extra SimPowerSystems license

## Slide 14: Model sharing and IP protection Protected model reference
>> pvinverter_det_vsub
1
Group the part(s) of the model you want to protect in a subsystem – note that only normal Simulink signals can be allowed to cross the subsystem boundaries

## Slide 15: Model sharing and IP protection Protected model reference
>> pvinverter_det_asub
2
Convert the subsystem to an Atomic unit
Block Parameters (Subsystem)
3
Specify the inport/outport signal attributes – data type, port dimensions, sample time, etc. – of the atomic unit explicitly
Create the appropriate <bus object> data type for any bus ports
4
Change the solver to FixedStepDiscrete
Add Rate Transition blocks where needed
Check the Inline parameters option
Configuration Parameters  Optimization  Signals…

## Slide 16: Model sharing and IP protection Protected model reference
>> pvinverter_det_mrefacc
5
Convert the subsystem to a Reference Model
Subsystem & Model Reference  Convert Subsystem to…
6
Switch the Simulation Mode of the referenced model to Accelerator
Block Parameters (ModelReference)
On the referenced model powergui  Configure parameters menu check the Use TLC file… option

## Slide 17: Model sharing and IP protection Protected model reference
7
>> pvinverter_det_pmref
Create the Protected Model
Subsystem & Model Reference  Create Protected Model …